SerialBuffer for orienteering radio transmission

1. Building a new project:
  1. https://www.mathaelectronics.com/raspberry-pi-pico-a-complete-guide/
  2. Based on the uart_advanced example
  3. Started a new workspace parallel to the pico_examples workspace
  4. Based in the uart_advanced example, but substituted the interrupt-driven UART R/w with a poll loop.
  5. The RP400 is connected directly to the DBG pins, so no additional Pico as debug interface.
  6. When debugging: Open pico_workspace/serialBuffer folder in vscode,
    1. Open pico_workspace/serialBuffer folder in vscode.
    2. Click the Debug icon in left pane
    3. Click the green play button on top of the pane.
2. SerialBuffer strucrture
  1. A ring buffer queue between Rx and Tx. The one used is not thread and interrupt safe, so need a better one.
  2. The queue is character based,not analyzing package structure.
  3. CTS/RTS: At the very least you will have to enable the CTS and RTS GPIO. You will then have to connect those GPIO to the external device.
    1. CTS is available on GPIO16.
    2. RTS is available on GPIO17.
    3. For UART 0 (I guess ttyS0) you will have to place those GPIO in mode ALT3. For UART 1 you will have to place those GPIO in mode ALT5.
    4. See page 102 of BCM2835 ARM Peripherals
    5. https://raspberrypi.github.io/pico-sdk-doxygen/group__hardware__gpio.html#ga2af81373f9f5764ac1a5bd6097477530
  4. Only enabling the handshake for the Tx, since we assume that the Rx must aways be ready.
3. Connections:

RP400 function	RP400 pin	Pico function	pico pin
DBG SWDIO	22	SWDIO	debug - SWDIO
DBG GND	20	GND	debug - GND
DBG CLK	18	CLK	debug - SWCLK
UART0 Tx	10	UART0 Rx	1
UART0 Rx	8	UART0 Tx	2
UART0 RTS	11	UART0 GP18 (TBD: UART0 CTS)	24 (TBD: 4)
GND		GND (for signals)	3
-	-	GND (for Power if not USB)	38
-	-	Power (if not USB): VSYS, 2 - 5.5 V	39

Note: I could not get the Pico HW UART0 CTS to function, so I use GP18 and testing for RTS in SW.

1. Test:
  1. The RP400 used as test machine
  2. A Python project "Serial Tester" sends data packages, blocking the Rx channel to fill the buffer. Then It reads the whole buffer, comparing the Rx data to an internal test buffer.
  3. various buffer levels are tested, ending with an overfilled buffer to force the test to fail, validating the test method.
2. TBD:
  1. Pico HW UART CTS operation. Otherwise move handshake input from GP18 to GP2 on Pico pin 4, so one compact connector may be used on pins 1,2,3,4.
  2. Interrupt driven operation, at least for the Rx side.
  3. Improved LED indications: sine heartbeat when idle, long ON and OFF pulses for Tx/Rx